## Slide 1: Routing Concepts
Prepared by
Risala Tasin Khan
Professor
IIT, JU

## Slide 2: Router as a Computer
Routers are
  Computers that specialize in sending packets over the data network
  They are responsible for interconnecting networks by selecting the best path for a packet to travel and forwarding packets to their destination
Routers are the network center
  Routers generally have 2 connections:
    WAN connection (Connection to ISP)
    LAN connection

## Slide 3: General Role of the Router
Connections of a Router for WAN
  A router has a DB-60 port that can support 5 different cabling standards
Connections of a Router for Ethernet
  2 types of connectors can be used: Straight through and Cross-over
    Straight through used to connect:
      Switch-to-Router, Switch-to-PC, Router-to-Server, Hub-to-PC, Hub-to-Server
    Cross-over used to connect:
      Switch-to-Switch, PC-to-PC, Switch-to-Hub, Hub-to-Hub, Router-to-Router

## Slide 4: Router as a Computer
Routers examine a packet’s destination IP address and determine the best path by enlisting the aid of a routing table

## Slide 5: Router as a Computer
Router components and their functions:
  CPU - Executes operating system instructions
  Random access memory (RAM) - Contains the running copy of configuration file. Stores routing table. RAM contents lost when power is off.
  Read-only memory (ROM) - Holds diagnostic software used when router is powered up. Stores the router’s bootstrap program.
  Non-volatile RAM (NVRAM) - Stores startup configuration. This may include IP addresses (Routing protocol, Hostname of router).
  Flash memory - Contains the operating system (Cisco IOS).
  Interfaces - There exist multiple physical interfaces that are used to connect network. Examples of interface types:
    Ethernet / fast Ethernet interfaces
    Serial interfaces
    Management interfaces

## Slide 6: Router as a Computer
Router Interface is a physical connector that enables a router to send or receive packets
Each interface connects to a separate network
Consist of socket or jack found on the outside of a router
Types of router interfaces:
  Ethernet
  Fastethernet
  Serial
  DSL
  ISDN
  Cable

## Slide 7: Router as a Computer
Two major groups of Router Interfaces
  LAN Interfaces
    Are used to connect router to LAN network
    Has a layer 2 MAC address
    Can be assigned a Layer 3 IP address
    Usually consist of an RJ-45 jack
  WAN Interfaces
    Are used to connect routers to external networks that interconnect LANs
    Depending on the WAN technology, a layer 2 address may be used
    Uses a layer 3 IP address

## Slide 8: Basic Routing
The role of routing protocols is to learn about other networks dynamically, exchange routing information with other devices, and connect internal and/or external networks.
It is important to note that routing protocols DO NOT send packets across the network.
Their role is to determine the best path for routing.
Different routing protocols use different means of determining the best or most optimal path to a network or network node.
Some types of routing protocols work best in static environments or environments with few or no changes, but it might take a long time to converge when changes to those environments are made.
Other routing protocols, however, respond very quickly to changes in the network and can converge rapidly.
Network convergence occurs when all routers in the network have the same view and agree on optimal routes.
When convergence takes a long time to occur, intermittent packet loss and loss of connectivity may be experienced between remote networks.
Notes: Network convergence refers to the provision of telephone, video and data communication services within a single network. In other words, one company provides services for all forms of communication.

## Slide 9: Packet Forwarding
Packet forwarding involves two processes:
  Determining the best path
  Sending the packet (switching)
When the router receives a packet for a directly connected network, the router checks the routing table and then the packet is forwarded to that network,

## Slide 10: Packet Forwarding (cont..)
If the packet is destined for a remote network, the routing table is checked and if there is a route or default route, the packet is forwarded to the next-hop router as shown in the figure

## Slide 11: Packet Forwarding (Cont..)
If the packet is destined for a network not in the routing table and no default route exists then it is dropped, as shown in Figure

## Slide 12: Internet Protocol Routing Fundamentals
A routing protocol allows a router to learn dynamically how to reach other networks.
A routing protocol also allows the router to exchange learned network information with other routers or hosts.
we can classify routing algorithms is according to whether they are global or decentralized:
A global routing algorithm
  computes the least-cost path between a source and destination using complete, global knowledge about the network.
  That is, the algorithm takes the connectivity between all nodes and all link costs as inputs.
  This then requires that the algorithm somehow obtain this information before actually performing the calculation. The calculation itself can be run at one site (a centralized global routing algorithm) or replicated at multiple sites.
  In practice, algorithms with global state information are often referred to as link-state (LS) algorithms, since the algorithm must be aware of the cost of each link in the network.

## Slide 13: Cont…
decentralized routing algorithm:
  The calculation of the least-cost path is carried out in an iterative, distributed manner.
  No node has complete information about the costs of all network links. Instead, each node begins with only the knowledge of the costs of its own directly attached links.
  Then, through an iterative process of calculation and exchange of information with its neighboring nodes (that is, nodes that are at the other end of links to which it itself is attached), a node gradually calculates the least-cost path to a destination or set of destinations.
  The decentralized routing algorithm is called a distance-vector (DV) algorithm, because each node maintains a vector of estimates of the costs (distances) to all other nodes in the network

## Slide 14: Cont…
A second broad way to classify routing algorithms is according to whether they are static or dynamic.
In static routing algorithms, routes change very slowly over time, often as a result of human intervention (for example, a human manually editing a router’s forwarding table).
Dynamic routing algorithms change the routing paths as the network traffic loads or topology change.
  A dynamic algorithm can be run either periodically or in direct response to topology or link cost changes.
  While dynamic algorithms are more responsive to network changes, they are also more susceptible to problems such as routing loops and oscillation in routes.

## Slide 15: Cont…
A third way to classify routing algorithms is according to whether they are load sensitive or load-insensitive.
In a load-sensitive algorithm, link costs vary dynamically to reflect the current level of congestion in the underlying link.
If a high cost is associated with a link that is currently congested, a routing algorithm will tend to choose routes around such a congested link.
Today’s Internet routing algorithms (such as RIP, OSPF, and BGP) are load-insensitive, as a link’s cost does not explicitly reflect its current (or recent past) level of congestion

## Slide 16: Administrative Distance
Administrative distance is used to determine the reliability of one source of routing information from another.
Some sources are considered more reliable than others are; therefore, administrative distance can be used to determine the best or preferred path to a destination network or network node when there are two or more different paths to the same destination from two or more different routing protocols.
The administrative distance is a locally significant value that affects only the local router.
This value is not propagated throughout the routing domain.
Therefore, manually adjusting the default administrative distance for a routing source or routing sources on a router affects the preference of routing information sources only on that router.
The smaller the administrative distance value, the more reliable the protocol. For example, if a router receives a route to a certain network from both Open Shortest Path First (OSPF) (default administrative distance - 110) and Interior Gateway Routing Protocol (IGRP) (default administrative distance - 100), the router chooses IGRP because IGRP is more reliable. This means the router adds the IGRP version of the route to the routing table.

## Slide 17: Router Paths and Packet Switching
A Metric is a numerical value used by routing protocols help determine the best path to a destination
  The smaller the metric value the better the path
2 types of metrics used by routing protocols are:
  Hop count - this is the number of routers a packet must travel through to get to its destination
  Bandwidth - this is the “speed” of a link also known as the data capacity of a link

## Slide 18: Router Paths and Packet Switching
Equal cost metric is a condition where a router has multiple paths to the same destination that all have the same metric
To solve this dilemma, a router will use Equal Cost Load Balancing - this means the router sends packets over the multiple exit interfaces listed in the routing table.

## Slide 19: Router Paths and Packet Switching
Path determination is a process used by a router to pick the best path to a destination
One of 3 path determinations results from searching for the best path
  Directly connected network
  Remote network
  No route determined

## Slide 20: Router Paths and Packet Switching
Switching Function of Router is the process used by a router to switch a packet from an incoming interface to an outgoing interface on the same router
  A packet received by a router will do the following:
    Strips off layer 2 headers
    Examines destination IP address located in Layer 3 header to find best route to destination
    Re-encapsulates layer 3 packet into layer 2 frame
    Forwards frame out exit interface

## Slide 21: Router Paths and Packet Switching
As a packet travels from one networking device to another
  The Source and Destination IP addresses NEVER change
  The Source & Destination MAC addresses CHANGE as packet is forwarded from one router to the next
  TTL field decrement by one until a value of zero is reached at which point router discards packet (prevents packets from endlessly traversing the network)

## Slide 22: Router Paths and Packet Switching
Path determination and switching function details. PC1 wants to send something to PC 2.
  Step 1 - PC1 encapsulates packet into a frame - frame contains R1’s destination MAC address

## Slide 23: Router Paths and Packet Switching
Step 2 - R1 receives Ethernet frame
  R1 sees that destination MAC address matches its own MAC
  R1 then strips off Ethernet frame
  R1 Examines destination IP
  R1 consults routing table looking for destination IP
  After finding destination IP in routing table, R1 now looks up next hop IP address
  R1 re-encapsulates IP packet with a new Ethernet frame
  R1 forwards Ethernet packet out Fa0/1 interface

## Slide 24: Router Paths and Packet Switching

## Slide 25: Router Paths and Packet Switching
Step 3 - Packet arrives at R2
  R2 receives Ethernet frame
  R2 sees that destination MAC address matches its own MAC
  R2 then strips off Ethernet frame
  R2 Examines destination IP
  R2 consults routing table looking for destination IP
  After finding destination IP in routing table, R2 now looks up next hop IP address
  R2 re-encapsulates IP packet with a new data link frame
  R2 forwards Ethernet packet out S0/0 interface

## Slide 26: Router Paths and Packet Switching
Step 4 - Packet arrives at R3
  R3 receives PPP frame
  R3 then strips off PPP frame
  R3 Examines destination IP
  R3 consults routing table looking for destination IP
  After finding destination IP in routing table, R3 is directly connected to destination via its fast Ethernet interface
  R3 re-encapsulates IP packet with a new Ethernet frame
  R3 forwards Ethernet packet out Fa0/0 interface
Step 5 - IP packet arrives at PC2 - frame is decapsulated and processed by upper layer protocols

## Slide 27
Some Basic Routing Commands

## Slide 28: Interfaces
Examining Router Interfaces
  Show IP router command – used to view routing table
  Show Interfaces command – used to show status of an interface
  Show IP Interface brief command – used to show a portion of the interface information
  Show running-config command – used to show configuration file in RAM

## Slide 29: Interfaces
Configuring an Ethernet interface
  By default all serial and Ethernet interfaces are down
  To enable an interface use the No Shutdown command

## Slide 30: Interfaces
Verifying Ethernet interface
  Show interfaces for fastEthernet 0/0 – command used to show status of fast Ethernet port
  Show ip interface brief
  Show running-config
Ethernet interfaces participate in ARP

## Slide 31: Interfaces
Configuring a Serial interface
  Enter interface configuration mode
  Enter in the ip address and subnet mask
  Enter in the no shutdown command
Example:
  R1(config)#interface serial 0/0
  R1(config-if)#ip address 172.16.2.1 255.255.255.0
  R1(config-if)#no shutdown

## Slide 32: Interfaces
Configuring a Serial interface
  Enter interface configuration mode
  Enter in the ip address and subnet mask
  Enter in the no shutdown command
Example:
  R1(config)#interface serial 0/0
  R1(config-if)#ip address 172.16.2.1 255.255.255.0
  R1(config-if)#no shutdown

## Slide 33: Routing Table and CDP Protocol
When a router only has its interfaces configured & no other routing protocols are configured then:
  The routing table contains only the directly connected networks
  Only devices on the directly connected networks are reachable

## Slide 34: Static Routes with Exit Interfaces
Purpose of a static route
  A manually configured route used when routing from a network to a stub network

## Slide 35: Static Routes with Exit Interfaces
IP route command
  To configure a static route use the following command: ip route
  Example:
    Router(config)# ip route network-address subnet-mask {ip-address | exit-interface }

## Slide 36: Static Routes with Exit Interfaces
Dissecting static route syntax
  ip route - Static route command
  172.16.1.0 – Destination network address
  255.255.255.0 - Subnet mask of destination network
  172.16.2.2 - Serial 0/0/0 interface IP address on R2, which is the "next-hop" to this network

## Slide 37: Static Routes with Exit Interfaces
Configuring routes to 2 or more remote networks
  Use the following commands for R1
    R1(config)#ip route 192.168.1.0 255.255.255.0 172.16.2.2
    R1(config)#ip route 192.168.2.0 255.255.255.0 172.16.2.2

## Slide 38: Static Routes with Exit Interfaces
Zinin’s 3 routing principles
  Principle 1: “Every router makes its decision alone, based on the information it has in its own routing table.”
  Principle 2: “The fact that one router has certain information in its routing table does not mean that other routers have the same information.”
  Principle 3: “Routing information about a path from one network to another does not provide routing information about the reverse, or return path.”

## Slide 39: Static Routes with Exit Interfaces
Modifying Static routes
  Existing static routes cannot be modified. The old static route must be deleted by placing no in front of the ip route
  Example:
    no ip route 192.168.2.0 255.255.255.0 172.16.2.2
  A new static route must be rewritten in the configuration

## Slide 40: Static Routes with Exit Interfaces
Verifying the Static Route Configuration
  Use the following commands
    Step 1 show running-config
    Step 2 verify static route has been entered correctly
    Step 3 show ip route
    Step 4 verify route was configured in routing table
    Step 5 issue ping command to verify packets can reach destination and that Return path is working

## Slide 41: Default Route
Default Static Route
  This is a route that will match all packets. Stub routers that have a number of static routes all exiting the same interface are good candidates for a default route.
    Like route summarization this will help reduce the size of the routing table.
Configuring a default static route
  Similar to configuring a static route. Except that destination IP address and subnet mask are all zeros.
  Example:
    Router(config)#ip route 0.0.0.0 0.0.0.0 [exit-interface | ip-address ].

## Slide 42: Default Route
Static routes and subnet masks
  The routing table lookup process will use the most specific match when comparing destination IP address and subnet mask
Default static routes and subnet masks
  Since the subnet mask used on a default static route is 0.0.0.0 all packets will match

## Slide 43: Static Routes and Packet Forwarding
Packet forwarding with static routes (recall Zinin’s 3 routing principles)
Router 1
  Packet arrives on R1’s Fastethernet 0/0 interface
  R1 does not have a route to the destination network, 192.168.2.0/24
  R1 uses the default static route

## Slide 44: Static Routes and Packet Forwarding
Packet forwarding with static routes (recall Zinin’s 3 routing principles)
Router 2
  The packet arrives on the Serial 0/0/0 interface on R2
  R2 has a static route to 192.168.2.0/24 out Serial0/0/1

## Slide 45: Static Routes and Packet Forwarding
Packet forwarding with static routes. (recall Zinin’s 3 routing principles)
Router 3
  The packet arrives on the Serial0/0/1 interface on R3
  R3 has a connected route to 192.168.2.0/24 out Fastethernet 0/1

## Slide 46: Static Routes and Packet Forwarding
Troubleshooting a Missing Route
Tools that can be used to isolate routing problems include:
  Ping - tests end to end connectivity
  Traceroute - used to discover all of the hops (routers) along the path between 2 points
  Show IP route - used to display routing table & ascertain forwarding process
  Show ip interface brief - used to show status of router interfaces
  Show cdp neighbors detail - used to gather configuration information about directly connected neighbors

## Slide 47: Static Routes and Packet Forwarding
Solving a Missing Route
Finding a missing or mis-configured route requires methodically using the correct tools
  Start with PING - if ping fails then use traceroute to determine where packets are failing to arrive
Issue: show ip route to examine routing table
  If there is a problem with a mis-configured static route remove the static route then reconfigure the new static route

## Slide 48: Static Routes and Packet Forwarding
Solving a Missing Route