## Slide 1: Configuring Router
Dr. Risala T Khan
Professor
IIT, JU

## Slide 2: Objective
Configure WAN Interface
Configure Static Routing Protocol

## Slide 3: What is DCE & DTE
The term DTE (Data Terminal EQUIPMENT) is used to describe the initiator or controller of the serial connection, typically the computer.
The term DCE (Data Communications EQUIPMENT) describes the device that is connected to the DTE device such as a modem.
The terms are most often used in reference to serial communications defined by the EIA RS232 standard.
Devices that communicate over a serial interface are divided into two classes: DTE and DCE.
The most important difference between these types of devices is that the DCE device supplies the clock signal that paces the communications on the bus.

## Slide 4: Topology
Device | Connected To | Connect From | IP Address
PC0 | Switch | Fast Ethernet 0/1 | 192.168.1.2/24
PC1 | Switch | Fast Ethernet 1/1 | 192.168.1.3/24
Router1 | Fast Ethernet 2/1 | Fast Ethernet 0/0 | 192.168.1.1/24
Router1 | Serial2/0 | Router 2’s Serial2/0 | 192.168.3.1/24
Router2 | Router1’s Serial 2/0 | Serial 2/0 | 192.168.3.2/24
Router2 | Fast Ethernet 0/0 | PC3 | 192.168.2.1/24
PC3 | Router2 | Fast Ethernet 0/0 | 192.168.2.3

## Slide 5: Class Work
Design the topology using the given table in your packet tracer
Notes: Max given time: 5min

## Slide 6: Configuring WAN Interface of Router1
Step | Command | Purpose
S1 | configure terminal Example: Router1# configure terminal | Enters global configuration mode.
S2 | interface serial slot/port Example: Router1(config)# interface serial 2/0 | Enters the configuration mode for a serial interface on the router.
S3 | ip address ip-address mask Example: Router1(config-if)# ip address 192.168.3.1 255.255.255.0 | Sets the IP address and subnet mask for the specified serial interface.
S4 | Clock rate Example: Router1(config-if)#Clock rate 56000 | For DCE part need to enter clock rate which can be 64000/72000/56000 or any Note: if one port is DCE and given clock rate then the other port must be DTE and for that port clock rate is not required
S5 | no shutdown Example: Router1(config-if)# no shutdown | Enables the GE interface, changing its state from administratively down to administratively up.
S6 | Exit Example:Router1(config-if)# exit | Exits configuration mode for the serial interface and returns to global configuration mode.

## Slide 7: Class Work
Configure WAN interface of Router2
Configure Fast Ethernet Interface of Both Router 1 & 2
Configure PC0, PC1 and PC3
Ping PC0 to PC1
Ping PC0 to Router1
Ping PC0 to PC3
FACING ANY PROBLEM!!!!!!!!
Notes: Max given time 25min

## Slide 8: Troubleshooting
From PC0 and PC1 provide “default gateway” address as “192.168.1.1”
From PC3 provide “default gateway” address as “192.168.2.1”
Configure Routers with Static Routing Protocol

## Slide 9: For Static Routing
Step | Command | Purpose
S1 | configure terminal Example: Router1# configure terminal | 
S2 | ip route prefix mask {ip-address ¦ interface-type interface-number [ip-address]} Example: Router1(config)# ip route 192.168.2.0 255.255.255.0 192.168.3.2. | Specifies the static route for the IP packets.
S3 | end Example: Router(config)# end | Exits router configuration mode, and enters privileged EXEC mode.
FOR ROUTER1
Configure Router2 following the same steps
Notes: Max given time 15

## Slide 10: To Verify
To verify that you have properly configured static routing, enter the “show ip route” command and look for static routes signified by the “S.”
You should see verification output similar to the following:

## Slide 11: Configure Default Route
Static routing solves one more network problem.
It can redirect all unmatched packets to a certain port.
We can set a default route for internet connection or we can implement a security measurement to deal with all matched packet.
By default, Routers are configured to drop the packet if destination address is not found in routing table.
Default route will override this behaviour.
If no match for destination network is found in routing table then it would be forwarded to the default route.
Thus default route is a way to deal with all unmatched packets.

## Slide 12
Step | Command | Purpose
S1 | Router(config)#ip route 0.0.0.0 0.0.0.0 ip_address_of_next_hop_neigher For example: Router1(config)# ip route 0.0.0.0 0.0.0.0 192.168.3.2. | Command to set default route. Here destination network to 0.0.0.0/0 represents all networks

## Slide 13: Class work
Ping from PC0 to PC3

## Slide 14: Home Work (Using the following table information design a network and ping from any device to any other device)
Device | Connected from | Connected to | IP Address
PC0 | FastEthernet0 | Router0’s FastEthernet0/0 | 10.0.0.2/8
Router0 | FastEthernet0/0 | PC0’s FastEthernet0 | 10.0.0.1/8
Router0 | Serial 0/0/0 | Router1’s serial0/0/0 | 192.168.0.253/30
Router1 | Serial0/0/0 | Router0’s Serial0/0/0 | 192.168.0.254/30
Router1 | Serial0/0/1 | Router2’s Serial0/0/0 | 192.168.0.249/30
Router2 | Serial0/0/0 | Router1’s Serial0/0/1 | 192.168.0.250/30
Router2 | Serial0/0/1 | Router3’s Serial0/0/0 | 192.168.0.245/30
Router3 | Serial0/0/0 | Router2’s Serial0/0/1 | 192.168.0.246/30
Router3 | FastEthernet0/0 | PC1’s FastEthernet0 | 20.0.0.1/8
PC1 | FastEthernet0 | Router1’s FastEthernet0/0 | 20.0.0.2/8