## Slide 1
IT-1101: IT Fundamentals
for
1st Year 1st Semester of B.Sc (Honors) in IT (10th Batch)
Lecture: 06
Output Fundamentals
Prepared by:
K M Akkas Ali
akkas_khan@yahoo.com, akkas@juniv.edu
Assistant Professor
Institute of Information Technology (IIT)
Jahangirnagar University, Dhaka-1342

## Slide 2
Lecture-06: Output Fundamentals
Topics to be Discussed
6.1 | Common Functions and Categories of Output Device | 
 | 6.1.1 | Definition
 | 6.1.2 | Common Functions of an Output Device
 | 6.1.3 | Categories of Output Device
 | 6.1.4 | I/O Devices
6.2 | Printer and its Usage | 
 | 6.2.1 | Terms Related to a Printer
 | 6.2.2 | Classification of Printers
 | 6.2.3 | Differentiate between Impact and Non-impact Printers
 | 6.2.4 | Factors for Choosing a Printer
6.3 | Monitor and its Usage | 
 | 6.3.1 | CRT Vs. LCD Monitors
 | 6.3.2 | Screen Clarity: Resolution, Refresh Rate and Dot Pitch
 | 6.3.3 | Factors for Choosing a Monitor
 | 6.3.4 | Significant of Display Adapter
6.4 | Audio Output Devices | 

## Slide 3
6.1 Common Functions and Categories of Output Device
6.1.1 | Definition of an Output Device
An output device is any device used to send information from a computer to another device or user.
An output device receives results from the processor usually for display, projection, or physical reproduction.
It provides a means to interact users with the computer.
The most commonly used output device on a computer is monitor. However, there are other output devices also.
Keep in mind that devices such as a CD, DVD, Floppy diskette, Pen Drive etc. may be capable of receiving information from the computer, but they are not output devices. These are considered as storage devices.
Example of Some Output Devices:
monitor, printer, speaker, plotter, multimedia projector etc.

## Slide 4
6.1.2 | Functions of an Output Device
Following functions are performed by an output device:
An output device accepts the results produced by the computer (which are in coded form, and hence, can not be easily understood by human).
It converts these coded results to human acceptable form.
Finally it supplies the converted results to the user.
6.1 Common Functions and Categories of Output Device

## Slide 5
6.1.3 | Categories of Output Devices
Form of output can be of two types:
Hard Copy
Printed copy of output is called hardcopy.
Soft Copy
It is usually a screen-displayed output, which is transient and is lost when the computer is turned off. Audio or voice-form data produced by speaker is also referred to as the soft-copy output. This kind of output is not tangible, i.e. it can not be touched.
Various categories of output devices are:
Category | Example(s)
Hard-copy | Printer, Plotter etc.
Soft-copy | Monitor, Speaker, Multimedia Projector etc.
6.1 Common Functions and Categories of Output Device

## Slide 6
6.1.4 | I/O Devices
Those devices that perform input operations as well as output operations are termed as I/O devices (or, input/output devices).
As the name suggests, input/output devices are capable of sending data (output) to a computer and receiving data from a computer (input).
Example of Some I/O Devices:
Modem, Touch-screen, Soundcard, Headset, LAN Card, CD, DVD, Hard disk etc.
6.1 Common Functions and Categories of Output Device

## Slide 7
6.2 Printer and its Usage
6.2.1 | Terms Related to a Printer
Printer is the most popular and widely used output device that produces hard copy on paper.
Printers are designed for low-volume, short-turnaround print jobs.
The world's first computer printer was a 19th-century mechanically driven apparatus invented by Charles Babbage for his Difference Engine.
Local Printers:
These printers are attached to standalone computer which serve only the user of that computer.
Network Printers:
These printers have built-in network cards. They are connected to a network which can serve any user on the network.

## Slide 8
6.2 Printer and its Usage
6.2.1 | Terms Related to a Printer…
Photo Printers:
These printers are specifically designed to print high quality digital photos on paper.
Some photo printers do not need a computer for printing. They include slots for memory cards used by many digital cameras. Instead of connecting the printer to a computer, the user can simply remove memory card from the camera and plug it into the photo printer.
Image Quality
Image quality also known as print resolution, is usually measured in dpi (dots per inch).
Speed of a Printer
Printer’s speed is measured in the number of pages of text the computer can print each minute. Pages per minute is abbreviated as ppm.

## Slide 9
6.2 Printer and its Usage
6.2.1 | Terms Related to a Printer…
Printer Driver
A printer driver is a piece of software that converts the data to be printed to the form specific to a printer.
The purpose of printer drivers is to allow applications to do printing without being aware of the technical details of each printer model.
Printers have been supplied with drivers for the most popular applications.
Print Spooling
Spool is an acronym for simultaneous peripheral operations on-line. It refers to putting jobs in a buffer where a device can access them when it is needed.
In print spooling, documents to be printed are loaded into a buffer (usually an area on a disk), and then the printer pulls them off the buffer at its own rate. As a result, the user is free to perform other operations on the computer while the printing takes place in the background.
Spooling also lets users place a number of print jobs in a queue instead of waiting for each one to finish before specifying the next one.

## Slide 10
6.2.2 | Classification of Printers
6.2 Printer and its Usage
Printers are classified according to a number of criteria:
Classification of printers according to printing capability: 3 types
Character printers: which prints one character of text at a time.
Line printers: which prints one line at a time
Page printers: which prints one page of text at a time
Classification of printers according to technology used in printer manufacture: 2 types
Impact Printers
These printers make physical contact with paper while printing. Example: Typewriter, Line printers, dot matrix printers etc.
Non-Impact Printers
  These printers form characters and images on paper without making direct physical contact between printing mechanism and paper. Example: Laser printers, ink-jet printers, etc.

## Slide 11
6.2.3 | Differentiate Between Impact & Non-impact Printers
6.2 Printer and its Usage
Factors | Impact Printers | Non-impact Printers
1. Physical contact with paper | Yes | No
2. Making noise | Yes | Almost no
3. Printing quality (resolution) | Not good | Improved
4. Printing speed (ppm) | Slower | Faster
5. Maintenance cost | Low | High
6. Initial cost | Low | High
7. Type of papers needed | Any type | Special type
8. Examples | Dot-matrix printer, Daisy-wheel printer etc. | Laser printer, ink-jet printer etc.
Note:
Using the above differentiation, we can also make contrast between dot-matrix and laser printers.

## Slide 12
6.2.4 | Factors for Choosing a Printer
6.2 Printer and its Usage
In evaluating printers, four criteria are most important, these are:
Image Quality or Print Resolution:
The image quality or print resolution is usually measured in dpi (dots per inch). The more the dpi of a printer, the higher its image quality.
Speed:
Speed of a printer is measured by the number of pages per minute (ppm) the device can print. Note that the speed of a dot matrix printer is measured by cps (characters per second).
Initial Cost:
The cost of new printers has fallen dramatically while their capabilities and speed have improved.
Cost of Operation:
The cost of ink, ribbon, or toner and maintenance varies with the type of printer. The choice of papers can also affect the cost of operation.

## Slide 13
6.3 Monitor and its Usage
6.3.1 | CRT Vs. LCD Monitors
  Monitor is the most important, popular and widely used soft-copy output device with which users interact most often.
  Two important hardware devices determine the quality of the image a monitor displays:
  (i) the monitor itself and
  ii) the video controller.
  Types of Monitor:
  Two basic types of monitors are used with personal computers:
1. CRT (cathode ray tube) type monitor
2. LCD (liquid crystal display)
Either of these two type of monitors can be monochrome, grayscale (displaying varying intensities of gray against a white background) or color.

## Slide 14
6.3 Monitor and its Usage
6.3.1 | CRT Vs. LCD Monitors…
  CRT Monitor:
  This type of monitor looks a lot like a TV screen that uses a vacuum tube as a display screen.
  Merits of CRT Monitor:
  CRT monitor provides a bright, clear picture. In other words, its resolution is high.
  It is low in cost.
  Its viewing angle is wider.
  Demerits of CRT Monitor:
  This type of monitor is big in size and large in weight, hence difficult to move.
  It needs comparatively much space to be fitted on the desk.
  It requires a lot of power to run; hence, it is not practical for use with notebook computers.
  Much more radiation emits from this type of monitor.
  It generates excessive heat.

## Slide 15
6.3 Monitor and its Usage
6.3.1 | CRT Vs. LCD Monitors…
  LCD Monitor:
  It is a flat-panel monitor on which an image is created when the liquid crystal (that is normally transparent) becomes opaque when charged with electricity.
  Merits of LCD Monitor:
  LCD monitor is small in size and light in weight, hence it is easily portable.
  Low operating power is required to run this type of monitor; hence it is widely used with notebook computers.
  There is no radiation from this monitor.
  It needs comparatively less space to be fitted on the lap or desk.
  It generates less heat.
  Demerits of LCD Monitor:
  Image quality is not improved in this monitor, i.e. its resolution is poor.
  It is high in cost.
  It has a narrow viewing angle.

## Slide 16
6.3 Monitor and its Usage
6.3.1 | CRT Vs. LCD Monitors…
  Differentiate between CRT and LCD Monitors:
Criteria | CRT Monitor | LCD Monitor
1. Have radiation? | Yes | No
2. Image quality (resolution) | Improved | Poor
3. Heat generation | Excessive | Almost no
4. Viewing angle | Wider | Narrow
5. Power consumption | High | Low
6. Size | Bigger | Smaller
7. Weight | Greater | Lighter
8. Cost | Less | More
9. Space required on the desk | More | Less
10. Portability/ Move | Difficult | Easy

## Slide 17
6.3.2 | Screen Clarity
Even if the monitor looks good, you need to check the following most important screen clarity specifications:
Resolution
Refresh rate
Dot pitch
6.3 Monitor and its Usage

## Slide 18
6.3.2 | Screen Clarity…
Resolution:
Resolution is the degree of sharpness or clarity of an image.
A monitor’s actual resolution is determined by the video controller, not by the monitor itself.
Monitor’s resolution is determined by the number of pixels on the screen. The more pixels a monitor can display, the higher its resolution and the clearer its images appear.
Though more items can fit on the screen at higher resolutions, but the items appear smaller, resulting in eyestrain and squinting.
6.3 Monitor and its Usage

## Slide 19
6.3.2 | Screen Clarity…
Refresh Rate:
A monitor’s refresh rate is the number of times per second that the electron guns scan every pixel on the screen.
Refresh rate is measured in hertz (Hz) or in cycle per second. If a monitor’s refresh rate is 100 Hz, it means that the monitor refreshes its pixels 100 times per second.
If the screen is not refreshed often enough, it appears to flicker, and flicker is one of the main causes of eyestrain.
In general, a refresh rate of 72 Hz or higher should not cause eyestrain. Some monitors have different refresh rates for different resolutions.
6.3 Monitor and its Usage

## Slide 20
6.3.2 | Screen Clarity…
Dot Pitch:
In color monitor, every pixel consists of three dots- one red, one green and one blue. The distance between the like-colored dots of adjacent pixels on a color
6.3 Monitor and its Usage
monitor is called dot pitch. In other words, if you measure the distance between the red dots of two adjacent pixels, you are measuring the monitor’s dot pitch.
Dot pitch is measured as a fraction of a millimeter (mm). It can range from .15 mm (very fine) to .40 mm or higher (coarse).
As a general rule, the smaller the dot pitch, the finer and more detailed images will appear on the monitor. That is, the highest-resolution monitors have the smallest dot pitch.
A color monitor with dot pitch not greater than 0.28 mm is better.

## Slide 21
6.3.4 | Factors for Choosing a Monitor
When you buy a monitor, you must consider the following:
(i) Take a close look at the display.
Look at a screen of text and examine how crisp the letters are, especially near the corners of the screen.
If you are going to work with graphics, display a picture with which you are familiar and see whether the colors look accurate.
(iii) Size of the monitor:
With a large monitor, you can make the objects on the screen appear bigger or you can fit more of them on the screen. In other words, bigger is better, though bigger cost more. Monitors are measured diagonally.
(iv) Resolution.
(v) Refresh rate.
(vi) Dot pitch.
6.3 Monitor and its Usage

## Slide 22
6.4 Audio Output Devices
Speaker
Speaker is an output device that plays back sound or voice signals.
Sound card (an I/O device) receives the digitized form of audio data stored in the computer. It then translates the digitized sound into analog signal that can be sent to the speaker to play back.
Headphone
Headphone is a small pair of speakers attached to the headband for wearing on the head.
It allows the user to listen to audio output without disturbing others.
Headphone is helpful when playing audio might disturb other people.
It is also useful while using portable computers (e.g. laptop), which do not have very high-quality speakers.

## Slide 23
6.4 Audio Output Devices
Headset
It is an I/O device that features a microphone and one or two speakers mounted on a headband for wearing on the head.
Microphone of a headset is plugged into the soundcard’s microphone input, and speakers are connected to the soundcard’s speaker jack.
Headsets are useful for speech-recognition applications, making phone calls using computer, or participate in chatting, video and audio-conferencing etc.

## Slide 24
Discussion Points
1. Functions and Categories of Output Device
2. Printer and Its Usage
3. Monitor and Its Usage
4. Speaker, Headphone and Headset

## Slide 25
Thank you…
Have a question?