## Slide 1
IT-1101: IT Fundamentals
for
1st Year 1st Semester of B.Sc (Honors) in IT (10th Batch)
Lecture: 07
CPU Fundamentals
Prepared by:
K M Akkas Ali
akkas_khan@yahoo.com, akkas@juniv.edu
Assistant Professor
Institute of Information Technology (IIT)
Jahangirnagar University, Dhaka-1342

## Slide 2
Lecture-07: CPU Fundamentals
Topics to be Discussed
7.1 | CPU and its Functions | 
 | 7.1.1 | What does Processing Mean
 | 7.1.2 | Function of the CPU
 | 7.1.3 | Part of the CPU and Their Functions
7.2 | Processor Architecture | 
 | 7.2.1 | Upward Vs. Downward Compatibility
 | 7.2.2 | RISC Vs. CISC Processor
 | 7.2.3 | Coprocessor used in PC
 | 7.2.4 | Ways of Measuring the Processing Speed
7.3 | Bus System and Port Used in Microcomputer | 
 | 7.3.1 | Types of Bus and Their Role
 | 7.3.2 | Bus Standard/ Bus Architecture
 | 7.3.3 | Standard and Specialized Expansion Ports
7.4 | Factors Affecting the Processing Speed of a Computer | 

## Slide 3
7.1 CPU and its Functions
7.1.1 | What does Processing Mean
The procedure that transforms raw data into useful information is called processing.
Two components handle processing in a computer:
Processor (CPU)
Memory
Both of these two components are located on the computer’s main system board or Motherboard.

## Slide 4
7.1 CPU and its Functions
7.1.2 | Function of the CPU
CPU is sometimes referred to as the ‘brain’ or ‘heart’ of a computer system. It is the part of the computer that actually processes the data.
The primary functions of a CPU is listed below:
The CPU accepts data and instructions from the input device (or from the software stored in its memory).
It processes the data according to the given instructions.
Finally it stores the results of the operations in its memory or displays it in a suitable output media such as monitor, printer etc.
Beside processing, the CPU also-
Controls the flow of data throughout the system.
Control the operations of all other units of the system.
Places data in memory and retrieves them when needed.

## Slide 5
7.1 CPU and its Functions
7.1.3 | Part of the CPU & Their Functions
Every CPU has at least two basic parts:
Arithmetic and Logic Unit (ALU)
Control Unit
Moreover, memory is also referred to as the part of CPU.
The parts of the CPU are usually connected by an electronic highway known as ‘Bus’.
To temporarily store data and instructions, the CPU has high-speed special-purpose memory devices called ‘Registers’.

## Slide 6
7.1 CPU and its Functions
7.1.3 | Part of the CPU & Their Functions…
The primary functions of ALU is listed below:
All arithmetic calculations and logical decisions are performed in the ALU.
When needed for processing, ALU receives data and instructions (involving arithmetic or logical operations) from primary memory.
ALU temporarily sends back the partial results to the primary memory, until needed later.
After the processing is over, the ALU then sends the final result to the memory unit to be stored either permanently or temporarily.

## Slide 7
7.1 CPU and its Functions
7.1.3 | Part of the CPU & Their Functions…
The primary functions of Control Unit is listed below:
This unit controls and coordinates the activities of all other units of a computer system.
It takes instructions from the memory unit one at a time and interprets them. It then sends appropriate signals to all other units to cause the specific instruction to be executed.
According to the stored instructions, the control unit ensures that the right operation is done on the right data at the right time.
Control unit acts as a central nervous system although it does not perform any actual processing on the data.

## Slide 8
7.1 CPU and its Functions
7.1.3 | Part of the CPU & Their Functions…
The primary functions of Memory Unit is listed below:
Memory stores data and instructions received from the input device for processing.
It supplies information to the ALU when required.
It receives partial or final results from the ALU.
It supplies final results to the output device.

## Slide 9
7.2 Processor Architecture
7.2.1 | Upward Vs. Downward Compatibility
Upward or Forward Compatibility:
  It is the capability of a hardware device (or a software product) to interact successfully with all succeeding versions of software (or hardware device). This hardware device (or software product) is called upward compatible.
  Upward compatibility allows software written for a computer with a particular CPU, to work on computers with newer processors of the same family.
  It also allows the users of these computer systems to easily upgrade their system, without worrying about converting all their existing software.

## Slide 10
7.2 Processor Architecture
7.2.1 | Upward Vs. Downward Compatibility…
Downward or Backward Compatibility:
  It is the capability of a new hardware device (or new software product) to interact successfully with all the same software product (or hardware device) that its predecessor could. This hardware device (or software product) is called downward compatible.

## Slide 11
7.2 Processor Architecture
7.2.2 | RISC Vs. CISC Processor
CISC Processor (Complex Instruction Set Computer)
  It is a kind of microprocessor chip that typically contains 200 to 300 instructions in it.
  In this type of processor, the instruction sets are designed elaborately as complex way.
  Length of each instruction in this type of processor is of variable length.
  Variable length addressing modes are also used in CISC processor.
  The processors in IBM-compatible computers and Motorola 680x0 computers are CISC processors.

## Slide 12
7.2 Processor Architecture
7.2.2 | RISC Vs. CISC Processor…
RISC (Reduced Instruction Set Computer)
  A newer theory in microcomputer design holds that if the instruction set for the CPU is kept small and simple, each instruction will execute much faster, allowing the processor to complete more instructions during a given period.
  CPUs designed according to this theory are called RISC processor (Reduced Instruction Set Computer). In this type of processors, reduced number of instructions is used (less than 200).
  Length of each instruction in this type of processor is of equal/ fixed length.
  Fixed length addressing modes are also used.
  This type of processor is used in the PowerPC computers.
  RISC processor-based PC results in a faster and less expensive than that of CISC processor-based PC.

## Slide 13
7.2 Processor Architecture
7.2.3 | Coprocessor used in PC
  A co-processor is a separate instruction-set processor that is closely coupled to the CPU.
  Its purpose is to enhance the processing speed of the main processor (CPU).
  Complicated arithmetic operations like exponentiation and trigonometric functions are costly to implement in the CPU hardware, while software implementations of these operations are slow. An arithmetic or math coprocessor is used as the auxiliary processor to the CPU to provide fast, low-cost hardware implementations of these special math functions.
  Newer CPUs have math coprocessor built-in. Earlier CPUs did not have them, so many users choose to upgrade their machines by adding them.

## Slide 14
7.3 Bus System and Port Used in Microcomputer
7.3.1 | Types of Bus and Their Role
In microcomputer, the term ’bus’ refers to the paths between the components of a computer which carries all information and signals involved in the system operation.
There are three buses used in microcomputer:
Address Bus
Data Bus
Control Bus
Like the processor, the bus’s speed is measured in megahertz (MHz), because it has its own clock speed.

## Slide 15
7.3 Bus System and Port Used in Microcomputer
7.3.1 | Types of Bus and Their Role…
Address Bus:
This is a unidirectional bus that carries binary address outputs from the CPU to the memory or I/O elements.
  In a computer with 16-bit address bus, there are 216=65536 different possible addresses. Each of these addresses corresponds to one memory location or one I/O element.
  Address bus is important because the number of wires in it determines the maximum number of memory addresses.
  The bigger the address bus, the CPU can address more memory and hence the bigger memory size.
Figure-1: CPU-Memory Interconnection

## Slide 16
7.3 Bus System and Port Used in Microcomputer
7.3.1 | Types of Bus and Their Role…
Data Bus:
This is a bi-directional bus that carries data between the CPU and memory or I/O elements.
  An 8-wires (or 8-bit) data bus can move eight bits (1 byte) at a time, a 16-wires (or 16-bit) data bus can transfer 16 bits (2 bytes) at a time, a 32-wires (32-bit) data bus can transfer 32 bits (4 bytes) at a time.
  With a wider data bus, the computer can move more data in the same amount of time.
Therefore, the number of wires in the data bus affects the speed at which data can travel between hardware components.

## Slide 17
7.3 Bus System and Port Used in Microcomputer
7.3.1 | Types of Bus and Their Role…
Control Bus:
This bus carries control signals from the CPU to the memory or I/O devices.
  The signal of the control bus synchronizes the activities of the separate computer elements.
  The CPU sends some of these control signals (such as Read or Write) to the other elements to tell them what type of operation is currently in process.

## Slide 18
7.3 Bus System and Port Used in Microcomputer
7.3.2 | Principal Bus Standard/ Bus Architecture
ISA Bus (Industry Standard Architecture):
  This bus was developed by IBM (International Business Machine) for its personal computer.
  It is a 16 bit bus (At first it was 8 bit bus when developed)
  This bus is still used in many computers to attach slower devices (such as modems and input devices) to the CPU.
  It works significantly for 286 microprocessor-based computers.

## Slide 19
7.3 Bus System and Port Used in Microcomputer
7.3.2 | Principal Bus Standard/ Bus Architecture…
MCA Bus (Micro Channel Architecture)
  This bus was developed by IBM for its PS/2 microcomputer.
  It is a 32 bit bus
  Expansion cards designed for ISA bus or EISA bus do not run in the MCA bus slot.
  This bus was not backward compatible.
  It works significantly for 386 microprocessor-based computers.

## Slide 20
7.3 Bus System and Port Used in Microcomputer
7.3.2 | Principal Bus Standard/ Bus Architecture…
EISA Bus (Enhanced Industry Standard Architecture)
  This bus is developed by a consortium of hardware developers.
  It is a 32 bit bus
  Expansion cards designed for ISA bus will run in the EISA slots.

## Slide 21
7.3 Bus System and Port Used in Microcomputer
7.3.2 | Principal Bus Standard/ Bus Architecture…
PCI Bus (Peripheral Component Interconnect)
  This bus is designed by Intel Corporation
  It is a 64 bit bus
  This bus was “open domain” i.e. allowing anyone to use it without Intel’s permission or any payment to Intel.
  This bus integrates new data types, such as audio, video, and graphics.
  It is widely used in high-speed Pentium-based computers.

## Slide 22
7.3 Bus System and Port Used in Microcomputer
7.3.2 | Principal Bus Standard/ Bus Architecture…
USB Bus (Universal Serial Bus)
  This bus is connected to the PCI bus.
  USB was at first co-invented by Ajay Bhatt of Intel (an Indian-American computer architect) and the USB-IF (USB Implementers Forum, Inc). The organization is comprised of industry leaders like Intel, Microsoft, Compaq, LSI, Apple and Hewlett-Packard.
  Unlike the PCI bus, USB is a hot swappable bus. (Hot Swappable means, a user can connect and then disconnect a USB device without affecting the machine.
  It allows connecting lower speed I/O devices to PC such as mouse, keyboard, flash memory, etc. without having to go through a complex installation procedure.
  USB supports up to 127 devices connected in either a daisy chain or hub layout.

## Slide 23
7.3 Bus System and Port Used in Microcomputer
7.3.2 | Principal Bus Standard/ Bus Architecture…
PCMCIA Bus
  This bus was developed by the Personal Computer Memory Card International Association (PCMCIA).
  It is a 32 bit bus.
  It allows user to insert credit card-size peripherals such as memory cards, modems etc.
  It is an open domain (i.e. allowing anyone to use it without permission), nonproprietary bus standard.
  This bus is used for notebook, sub-notebook and palmtop computers.
  A card used in this bus is now called PC Card.

## Slide 24
7.3 Bus System and Port Used in Microcomputer
7.3.3 | Standard and Specialized Expansion Ports
A port is a socket on the outside of the system unit that is connected to an expansion board on the inside of the system unit.
  Ports allow connecting common devices to computer, such as monitor, printer, keyboard, modem, mouse, speaker etc.
  Some commonly used ports are listed below:
  Serial Port (also called COM port)
  Parallel Port
  Network Adapter Port/ Network Port
  Video Adapter Port/ Monitor Port
  Audio Port
  Modem Port
  Mouse and Keyboard Ports
  SCSI Port (Small Computer System Interface)
  USB Port (Universal Serial Bus)
  FireWire Port (IEEE 1394 Port)
Standard Ports
Specialized Ports

## Slide 25
7.4 Factors Affecting the Processing Speed of a Computer
The circuitry design of a CPU determines its basic speed, but several additional factors can increase the processing speed of a CPU. These factors are:
Size of the register of the CPU:
Size of memory (RAM)
Cache memory
Clock speed
Data bus
Address bus
Coprocessor

## Slide 26
Discussion Points
1. Elements of CPU and Their Functions
2. Types of processor: RISC Vs. CISC
3. Bus System and Port in Microcomputer
4. Factors Affecting the Processing Speed of a Computer

## Slide 27
Thank you…
Have a question?