## Slide 1
IT-1101: IT Fundamentals
for
1st Year 1st Semester of B.Sc (Honors) in IT (10th Batch)
Lecture: 08
Memory Fundamentals
Prepared by:
K M Akkas Ali
akkas_khan@yahoo.com, akkas@juniv.edu
Assistant Professor
Institute of Information Technology (IIT)
Jahangirnagar University, Dhaka-1342

## Slide 2
Lecture-08: Memory Fundamentals
Topics to be Discussed
8.1 | Definition and Function of a Memory | 
 | 8.1.1 | Definition
 | 8.1.2 | Common Functions of Memory
 | 8.1.3 | Capacity of a Memory
8.2 | Classification of Memory According to Various Criteria | 
 | 8.2.1 | Primary Vs. Secondary Memory
 | 8.2.2 | Volatile Vs. Non-Volatile Memory
 | 8.2.3 | Random Access Vs. Sequential Access Memory
 | 8.2.4 | Semiconductor Vs. Magnetic Vs. Optical Memory
 | 8.2.5 | RAM Vs. ROM and Their Types
 | 8.2.6 | Flash Memory
 | 8.2.7 | Cache Memory
 | 8.2.8 | Register
8.3 | CPU-Memory Interconnection | 
 | 8.3.1 | How does the CPU Write Data into Memory
 | 8.3.2 | How does the CPU Read Data from Memory

## Slide 3
8.1 Definition and Function of a Memory
8.1.1 | Definition of Memory
A memory is a device that is used for storing data or information either permanently or temporarily.
Example of Some Memory Devices:
RAM, ROM, Hard Disk, CD, DVD, Cache Memory, Pen drive etc.

## Slide 4
8.1.2 | Functions of Memory
The primary functions of Memory is listed below:
Memory stores data and instructions received from the input device for processing.
It supplies information to the ALU when required.
It receives partial or final results from the ALU.
It supplies final results to the output device.
Memory is needed for the following purposes:
i) To store the program and data during execution.
ii) To store the program for repetitive use.
iii) To store the data for future or periodical use.
iv) To store the result of execution.
8.1 Definition and Function of a Memory

## Slide 5
8.1.3 | Capacity of a Memory
Capacity of a memory is defined in terms of the number of bits that can be stored in that memory device.
Memory capacity is expressed in a number of units. Some of them are expressed below:
BIT:
It is the abbreviation of Binary Digit, which is either a 0 or a 1.
It is the smallest unit of information that can be stored by a digital computer. That is, either a 0 (zero) or a 1 (one) is called a bit.
Byte:
A combination of 8 bits is called a byte, i.e. 1 byte= 8 bits.
Nibble:
A collection of 4 bits is called a nibble, i.e. 1 nibble= 4 bits= ½ byte
8.1 Definition and Function of a Memory

## Slide 6
8.1.3 | Capacity of a Memory…
1 Byte = 8 Bit
1 KB (Kilobyte) = 1024 Byte
1 MB (Megabyte) = 1024 KB
1 GB (Gigabyte) = 1024 MB
1 TB (Terabyte) = 1024 GB
1 PB (Petabyte) = 1024 TB
1 EB (Exabyte) = 1024 PB
8.1 Definition and Function of a Memory

## Slide 7
8.2 Classification of Memory
Memory can be classified according to a number of criteria:
Storage capacity
The method of storing and retrieving data
The time needed to store and retrieve data
Connection of memory device with the CPU
Storing data temporarily or permanently
Cost per bit of storage etc.

## Slide 8
8.2 Classification of Memory
8.2.1 | Primary Vs. Secondary Memory
Primary Memory (Main Memory):
Primary memory is directly connected to the CPU.
Every location in main memory can be directly and randomly accessed by the CPU.
However, the primary memory can hold information only while the computer system in on. As soon as the computer system is switched off or reset, information stored in the primary memory disappears. Hence, primary memory is sometimes referred to as the volatile or temporary memory.
Moreover, primary memory normally has limited storage capacity, because it is very expensive.
The primary memory of modern computer system is made up of semiconductor devices.
This memory-
holds data and instructions before the actual processing starts
intermediate results of ongoing processing
final results of processing before being passed on to the output units.
Example of primary memory: RAM, ROM.

## Slide 9
8.2 Classification of Memory
8.2.1 | Primary Vs. Secondary Memory…
Secondary Memory (Auxiliary Memory):
Secondary memory is used for storing programs and large data files which are currently not required by the CPU, but at later time they may be needed for processing.
This memory can retain information even when the computer system is switched off or reset, i.e. it holds data permanently.
It is much larger in capacity but much slower than main memory.
It also serves as an overfollow memory when the capacity of the main memory is exceeded.
Secondary memories that have huge capacity are termed as bulk memory or storage.
Example of secondary memory: hard disk, compact disk (CD), digital versatile disk (DVD), Pendrive, etc.

## Slide 10
  Differentiate between Primary and Secondary Memory
Criteria | Primary Memory | Secondary Memory
Connection of memory to the CPU? | Directly | Indirectly
Store data temporarily or permanently? | Temporarily (i.e. volatile) | Permanently (i.e. non-volatile)
What data and information it stores? | It holds data and instructions on which the CPU is currently working. | It holds data and information which are not currently required by the CPU
Access time (time required to load data from the memory into register) | Less | Much
Speed | Higher | Lower
Cost per bit | High | Low
Storage capacity | Limited | High
Examples | RAM | Hard disk, CD, DVD etc
8.2 Classification of Memory
8.2.1 | Primary Vs. Secondary Memory…

## Slide 11
8.2 Classification of Memory
8.2.2 | Volatile Vs. Non-Volatile Memory
Memory can also be classified into two categories whether data, stored on it, retains even when the power is turned off or interrupted.
Volatile or temporary memory (e.g. RAM, Cache Memory, Register etc.)
Non-volatile or permanent memory (e.g. Harddisk, CD, DVD, Pendrive etc.)

## Slide 12
8.2 Classification of Memory
8.2.2 | Volatile Vs. Non-Volatile Memory…
Volatile (or Temporary) Memory:
A memory is said to be volatile memory if the stored information is destroyed when power goes off.
In almost all computer systems, the primary memory is volatile and the secondary memory is non-volatile. ROM is the exception in this case, though it is a primary memory, but non-volatile in nature.
Example of volatile memory: RAM, cache memory, register etc.
Non-Volatile (or Permanent) Memory:
Nonvolatile memory can retain data stored on it, even when the power is turned off or interrupted.
In almost all computer systems, the primary memory is volatile and the secondary memory is nonvolatile.
Example of nonvolatile memory: hard disk, floppy disk, compact disk (CD), digital versatile disk (DVD), ROM etc.

## Slide 13
8.2 Classification of Memory
8.2.3 | Random Access Vs. Sequential Access Memory
Memory can also be classified into two categories whether the time taken to access a piece of data from the memory unit is independent or dependent of the location of the data in the memory unit.
Random Access Memory (e.g. RAM and ROM)
Sequential Access Memory (SAM) (e.g. Magnetic Tape Memory)

## Slide 14
8.2 Classification of Memory
8.2.3 | Random Access Vs. Sequential Access Memory…
Random Access Memory:
In this type of memory, any location can be directly accessed by the CPU.
Time taken to access a piece of data from this memory unit is independent of the location of the data in the memory. In other word, the access time is the same for any address in memory.
Data can be read from or written into this memory.
In almost all computer systems, the primary memory has random access property.
Example: RAM and ROM

## Slide 15
8.2 Classification of Memory
8.2.3 | Random Access Vs. Sequential Access Memory…
Sequential Access Memory:
It is a type of memory in which the access time is not constant, but varies depending on the storage location of the data.
A particular stored word is found by sequencing through all address location until the desired address is reached. This produces access time, which are much longer than those of random access memory.
Example: Magnetic tape memory.

## Slide 16
8.2 Classification of Memory
8.2.4 | Semiconductor Vs. Magnetic Vs. Optical Memory
Memory can also be classified into three categories according to manufacturing technology of how data is stored in the memory.
These are:
Semiconductor memory
Magnetic memory
Optical memory

## Slide 17
8.2 Classification of Memory
8.2.4 | Semiconductor Vs. Magnetic Vs. Optical Memory
Semiconductor Memory
This type of memory stores data in the form of electrical charge or voltage.
Due to the high speed, small size and volatile nature, it is used as the primary internal memory of a computer.
Examples: RAM, ROM, Register, Cache Memory etc.
Magnetic Memory
This memory stores data in magnetic form rather than electronic form.
Due to low cost and high storage capacity, this memory is used as the external storage memory of a computer.
Examples: Magnetic tape memory, Magnetic disk memory (e.g. hard disk, floppy disk), magnetic core memory etc.
Optical Memory
This memory stores data in optical form rather than electronic or magnetic form. It uses a laser beam to write or read onto a specially coated disk.
This type of memory is relatively low in cost, but immune to dust.
Examples: Compact disk (CD), Digital versatile disk (DVD).

## Slide 18
8.2 Classification of Memory
8.2.5 | RAM Vs. ROM
Random Access Memory (RAM):
This is a type of random access memory in which data can be read from or written into.
All data stored in RAM will be lost if power is interrupted or turned off. Hence, it is called volatile or temporary memory.
RAM stores data and instructions on which the CPU is currently working on.
Generally, the more RAM a computer has, the more it can do and the faster it can perform certain tasks.
Read Only Memory (ROM):
This is a type of random access memory in which data can only be read from.
Data stored in ROM will not be lost when power is interrupted or turned off. Hence, it is a nonvolatile memory.
It holds data that either are permanent or will not change frequently during the operation of a system.
Technically, a ROM can be written into (programmed) only once and this operation is normally performed at the factory. Therefore no new data can be written into a ROM but data can be read from ROM.
Some ROMs can be written into more than once.

## Slide 19
8.2 Classification of Memory
8.2.5 | RAM Vs. ROM…
Factors | RAM | ROM
1. Is it possible to read, and/or write? | Both (i.e. information can be written into or read from it). | Information can only be read from this memory.
2. Store data temporarily or permanently? | Temporarily (i.e. RAM is volatile) | Permanently (i.e. ROM is non-volatile)
3. Is data lost when power goes off? | Yes | No
4. What data and information it stores? | It holds data and instructions that are subject to change frequently during system operation. | It holds information which is not changed during system operation, but necessary to run the system.
Differentiate between RAM and ROM

## Slide 20
8.2 Classification of Memory
8.2.5 | RAM Vs. ROM…
Types of RAM
Static RAM (SRAM):
This RAM can store data as long as power is not interrupted, without the need for periodically rewriting the data into memory.
The main applications of SRAM are in areas where only small amounts of memory are needed or where high speed is required. SRAM is more speedy than DRAM.
SRAM has the disadvantage of being costlier and having low power packing density.
Dynamic RAM (DRAM):
This RAM can also store data as long as power is applied, but the stored data will gradually disappear. So, it is necessary to periodically refresh the data to be reappeared.
The main internal memory of most personal computers uses DRAMs because of its high storage capacity and low power consumption.
The need for refreshing is a disadvantage of dynamic RAM because some external refreshing circuits is required.
Other types of RAM:
SDRAM (Synchronous Dynamic RAM), EDO RAM (Extended Data Output RAM)

## Slide 21
8.2.5 | RAM Vs. ROM…
Basically, there are two categories of ROM:
Manufacturer-programmed Read Only Memory
In this type of ROM, data is stored permanently by the manufacturer. It is not possible for a user to modify the programs stored inside the ROM chip.
For example, a PC manufacturer may store the system boot program permanently in the ROM chip used on the motherboard. Similarly, a printer manufacturer may store the printer controller software in the ROM chip used on the circuit board of the printer.
This ROM is also called MROM (mask read only memory) or just ROM.
User-programmed Rad Only Memory
In this type of memory, the user can store “read-only” programs and data on it.
Such a ROM is commonly known as PROM (programmable read-only memory), because, a user can program it.
Other kinds of user-programmed ROM are EPROM (erasable programmable read-only memory), EEPROM (electrically erasable programmable read-only memory).
8.2 Classification of Memory
Types of ROM:

## Slide 22
8.2.5 | RAM Vs. ROM…
Programmable Read Only Memory (PROM):
This ROM is user-programmable i.e. it is not programmed during the manufacturing process but are custom-programmed by the user.
Once programmed, a PROM cannot be erased or reprogrammed.
Thus, if the program in the PROM is faulty or has to be changed, the PROM has to be thrown away. For this reason, this memory is often referred to as ‘one time programmable’ ROM.
8.2 Classification of Memory
Types of ROM…

## Slide 23
8.2.5 | RAM Vs. ROM…
Erasable Programmable Read Only Memory (EPROM):
An EPROM can be programmed by the user and it can also be erased and reprogrammed as often as desired.
Once programmed, the EPROM is a nonvolatile memory that will hold its stored data indefinitely.
It can be erased by exposing it to ultraviolet light. Once erased, the EPROM can be reprogrammed.
EPROMs are used to store programs, which are permanent but need updating.
Since, the contents of EPROM are erased by exposing the memory chip for some time to ultraviolet light; it is often termed as ultra violet EPROM (UVEPROM).
8.2 Classification of Memory
Types of ROM…

## Slide 24
8.2.5 | RAM Vs. ROM…
Electrically Erasable Programmable ROM (EEPROM):
This ROM can be electrically programmed, erased and reprogrammed.
Contents in the EEPROM can be erased by using high voltage electric pulses.
In EEPROM, instead of erasing the entire contents of the chip, its contents may be erased block-wise.
It can be reprogrammed electrically either partly or fully.
Due to the ease with which stored programs can be altered, EEPROM is also known as flash memory, which is used in many new I/O and storage devices.
8.2 Classification of Memory
Types of ROM…

## Slide 25
8.2.5 | RAM Vs. ROM…
Difference Between EPROM and EEPROM:
EEPROM has the ability to electrically erase and reprogram individual words in the memory array.
It is possible to erase a selected memory cell in EEPROM but there is no way to erase a selected memory cell in EPROM, once erased, all contents of entire EPROM is erased.
It is easier to alter stored information from an EEPROM chip, as compared to EPROM.
An EEPROM can be erased and reprogrammed quickly and easily than the EPROM (10 ms vs. 30 minutes).
8.2 Classification of Memory
Types of ROM...

## Slide 26
Flash memory is a special type of memory chip that combines the best features of RAM and ROM.
Like RAM, flash memory lets a user (or program) access data randomly and it also lets the user overwrite any (or all) of its contents at any time. Like ROM, it is nonvolatile, so it retains data even when power is off.
Flash memory is often used in portable digital devices for storage like in digital camera, MP3 player, USB “keychain” storage device, game console etc.
8.2 Classification of Memory
8.2.6 | Flash Memory

## Slide 27
Moving data between RAM and the CPU’s registers is one of the most time-consuming operation a CPU must perform, simply because RAM is much slower than the CPU.
A partial solution to this problem is to include a Cache memory between the CPU and main memory.
Cache memory is used as a high speed buffer between the CPU and main memory for minimizing the memory-processor speed mismatch.
When a program is running and the CPU needs to read data or instructions from RAM, the CPU first checks to see whether the data or instruction is in cache memory. If the data that it needs is not there, it reads the data from RAM in to its registers but it also loads a copy of the data into the cache memory. The next time the CPU needs that same data, it finds it in the cache memory and saves the time needed to load the data from RAM. A frequently used program that needs a repeated operation is resided in cache memory.
8.2 Classification of Memory
8.2.7 | Cache Memory

## Slide 28
Register is the high-speed memory element that is built directly into the ALU part of the CPU.
It holds data and instructions temporarily that are currently being processed by the CPU.
The computer loads instruction and data from main memory into the registers just before processing, which helps the computer process faster.
The size of the registers (also called the word size) indicates the amount of data with which the computer can work at any given time.
The bigger the word size, the more quickly the computer can process a set of data.
64-bit processor, or 64-bit register or 64-bit computer means that the word size of the computer is 8 bytes.
Various types of registers used in a personal computer:
1) Memory Address Register (MAR) 2) Memory Buffer Register (MBR)
3) Program Control Register (PC) 4) Accumulator Register (AC),
5) Instruction Register (IR) 6) Input/Output Register (I/O)
8.2 Classification of Memory
8.2.8 | Register

## Slide 29
In order to process data or store the result of operation, the CPU frequently needs to access the memory using address bus, data bus and control bus.
The processes of writing data to memory and reading data from memory is illustrated below.
8.3 CPU Memory Interconnection
Figure-1: CPU-Memory Interconnection

## Slide 30
8.3 CPU Memory Interconnection…
Write Operation:
Step_1: The CPU supplies the binary address of the memory location where the data are to be stored. It places this address on the address bus lines.
Step_2: The CPU places the data to be stored on the data bus lines.
Step_3: The CPU activities the appropriate control signal (for this case, memory write operation) using the control bus.
Step_4: The memory decodes the binary address supplied by the CPU via address bus to determine to which location is being selected for the store operation.
Step_5: Finally, the data on the data bus are transferred to the selected memory location.
8.3.1 | How does the CPU write data into memory

## Slide 31
8.3 CPU Memory Interconnection…
Read Operation:
Step_1: The CPU supplies the binary address of the memory location from which data are to be retrieved. It places this address on the address bus lines.
Step_2: The CPU activates the appropriate control signal lines for the memory read operation.
Step_3: The memory IC decodes the binary address to determine which location is being selected for the read operation.
Step_4: The memory IC places data from the selected memory location on the data bus form where they are transferred to the CPU.
8.3.2 | How does the CPU read data from memory

## Slide 32
Discussion Points
1. Definition and Functions of a Memory
2. Primary Vs. Secondary Memory
3. RAM Vs. ROM
4. CPU-Memory Interconnection

## Slide 33
Thank you…
Have a question?