## Slide 1: Fourier Series & Transform
IT 3105: Signals and Systems

## Slide 2: Jean Baptiste Joseph Fourier
Jean Baptiste Joseph Fourier,a French mathematician and a physicist; was born in Auxerre, France.
He initialized Fourier series, Fourier transforms and their applications to problems of heat transfer and vibrations. The Fourier series, Fourier transforms and Fourier's Law are named in his honour.
Jean Baptiste Joseph Fourier, 21March1768– 16May1830

## Slide 3: Fourier Series
Fourier series can be used to expand the periodic signal in terms of harmonics which are sinusoidal and orthogonal to each other.
Periodic signals can be continuous or discrete. For continuous signal CTFS and for discrete signal DTFS can be derived.
Fourier Transform, CTFT and DTFT is used to analyze non-periodic signal. FS and FT is used for analysis purposes.
Signals can be in form of square, sine or cosine. Again a square wave can be formed using infinite number of sine wave. Fourier series can be used to decomposed these composite signals.
For modeling any odd signal we can use sine terms. [sin (-x)= -sin(x)]
For modeling any even signal we can use cosine terms. [cos(-x) = cos(x)]

## Slide 4: Dirichlet Condition
For any periodic signals we have to find “Dirichlet Condition” satisfied or not to prove the existence of Fourier series expansion.
  Periodic signals can be analyzed by FS if the Dirichlet Condition are satisfied by any periodic signal then we can say FS exists for that signal.
  Condition 1: Signals should have finite number of minima and maxima over the range of time period.
  Condition 2: Signal should have finite numbers of discontinuities over the range of time period.
  Condition 3: Signals should be absolutely integrable over the range of time period.

## Slide 5: Dirichlet Condition 1
Both signal x1(t) and x2(t) are periodic.
For x1(t), fundamental period is T0. We can see one minima and one maxima within FTP, i.e. condition 1 satisfied.
For x2(t), we can see infinite numbers of maxima and minima within FTP, i.e. condition 1 not satisfied. So we can not find FS expansion for x2(t).

## Slide 6: Condition 2
For x1(t), fundamental period is T0, there are 3 discontinuities, i.e. finite numbers of discontinuities within FTP.
Finally, we can say FS exists for x1(t).
For x2(t), fundamental period is T0 and we can infinite number of discontinuities over FTP.
There is no FS expansion for x2(t)

## Slide 7: Condition 3
When , i.e. finite then the signal is called absolutely integrable over the range of FTP.
For any PS signal which is not a energy signal,
  We can integrate them over time period,
  We can also integrate over FTP, ; which may or may not finite or infinite.
  For , we find it is absolutely integrable, i.e. finite integration.
  For , at FTP T0, we find that the signal is infinite, i.e. condition 3 is violated.

## Slide 8: Periodic Signals
A continuous-time signal x(t) to be periodic if there is a positive nonzero value of T for which
  x(t + T) = x(t) ;all t
The fundamental period T0 of x(t) is the smallest positive value of T and 1/T0 = f 0 is referred to as the fundamental frequency.

## Slide 9: Complex Exponential Fourier Series Representation
The complex exponential Fourier series representation of a periodic signal x( t) with fundamental period T0 is given by
where ck are known as the complex Fourier coefficients and are given by
where ∫To denotes the integral over any one period and 0 to C or -T0/2 to T0/2 is commonly used for the integration. Setting k = 0
  which indicates that c0 equals the average value of x(t) over a period.

## Slide 10: Complex Exponential Fourier Series Representation
We know for any periodic signal x(t), complex co-efficient of FS is given as ……(1)
To analyze the complex FS expansion, let us apply reversal on cn, i.e. k = ‒ k. We get . Now applying complex conjugate * operation we get …….(2)
If ck is conjugate symmetry, i.e. ; implies that , by observing equation (1) & (2). Finally we can cay x(t) is a real signal.
  For any real time domain signal, the exponential Fourier series co-efficient ck will be conjugate symmetric and vice verse is also true. Complex co-efficient can also expressed as
  ……(3); where is the magnitude and is the angle. Applying conjugate on we get …..(4) . As we know . So we can say
  and , when x(t) is real then the ck is conjugate symmetry, then the magnitude, is even and angle is odd in nature.

## Slide 11: Trigonometric Fourier Series
The trigonometric Fourier series representation of a periodic signal x(t) with fundamental period T0 is given by
  x(t) = dc/avg. values of x(t)+ cosine terms + sine terms
where ak and bk are the Fourier coefficients and the complex Fourier coefficients ck given by

## Slide 12: Coefficients of Trigonometric Fourier Series
DC value or average values of x(t), a0
Cosine part/ even part
Sine part/ odd part
Exp:
  In 2nd harmonics a2=3, b2=5; so b2>a2, i.e. sine terms are dominating here.
  In 3rd harmonics a3= 4, b3= 2; so a3>b3, i.e. cosine terms are dominating here.
  DC value: If x(t) is symmetrical about t-axis(x-axis), then a0 => 0, as the area will be zero, i.e. same portion of signal is found on positive and negative side.
    If x(t) is even then . If signal is odd signal then,

## Slide 13: Even and Odd Signals
If a periodic signal x(t) is even, then bk= 0 and its Fourier series contains only cosine terms:
If x(t) is odd, then ak = 0 and its Fourier series contains only sine terms

## Slide 14: Example
For x1(t)
  The signal is symmetrical about x- axis, so a0= 0
  Again, x1(t) is even signal, so bn= 0.
  Only an≠ 0, we need to calculate this part to expand the signal.
For x2(t)
  Again avg. value a0= 0
  The signal is odd so an= 0
  Only need to find the part bn≠ 0

## Slide 15: Harmonic Form Fourier Series
Another form of the Fourier series representation of a real periodic signal x(t) with fundamental period T0 is
The term C0 is known as the de component, and the term Ckcos(kw0t - (θk) is referred to as the kth harmonic component of x(t). The first harmonic component C1 cos(w0t - θ1) is commonly called the fundamental component because it has the same fundamental period as x(t). The coefficients Ck and the angles θk are called the harmonic amplitudes and phase angles, respectively, and they are related to the Fourier coefficients ak and bk by

## Slide 16: Relation between the coefficients of TFS and EFS

## Slide 17: The Fourier Transform
Spectrum of any nonperiodic signal is analyzed by Fourier transform/integral instead of Fourier series. Let us now consider a nonperiodic signal x(t), its Fourier integral/transform is expressed as,
Again its inverse Fourier transform is given as,
  Symbolically we can write, x(t) ↔ X(f)
  That is we can convert signals from time to frequency domain and vice-varsa.

## Slide 18: The Fourier Transform of rectangular pulse
Let us consider a rectangular pulse of width τ and height A shown in fig.
  Fourier transform of x(t),

## Slide 19: Inverse Fourier Transform
  Let X(ω) be the Fourier transform of an integrable continuous-time signal x(t).
  Under suitable condition, x(t) can be reconstructed from X(ω) using inverse Fourier transform , as:

## Slide 20: Properties of Fourier transform
  Let x(t), x1(t), x2(t) and x3(t) be four integrable continuous-time signals and their Fourier transforms are X(ω), X1(ω), X2(ω) and X3(ω) respectively.
  The Fourier transform has the following basic properties:
  Linearity:
  For any complex numbers a and b,
  a x1(t) + b x2(t)  a X1(ω) + b X2(ω)

## Slide 21: Properties of Fourier transform
  Time-shifting (Translation):
  For any real numbers t0, the time shift version of signal x(t) to to is x(t-t0). Then
  Equation (5.50) shows that the effect of a shift in the time domain is simply to add a linear term –ωt0 to the original phase spectrum θ(ω). This is known as a linear phase shift of the Fourier transform X(ω).
  Thus, time-shifting property shows that the multiplication of Fourier transform X(ω) of signal x(t) by a complex exponential signal ej ω0t is equal to the t0 shift of x(t) in time domain.

## Slide 22: Properties of Fourier transform
  Frequency-shifting (Modulation):
  For any real numbers ω0, if x(t) = ej ω0t x1(t), then X(ω) = X1(ω -ω0).
  The multiplication of x1(t) by a complex exponential signal ej ω0t is sometimes called complex modulation.
  Thus, frequency-shifting property shows that complex modulation in the time domain corresponds to a shift of X(w) in the frequency domain.
  Note that the frequency-shifting property is the dual of the time-shifting property.

## Slide 23: Properties of Fourier transform
  Time Scaling:
  For a non-zero real number a, the time scale version of signal x(t) is x(at), then
  The above equation indicates that scaling the time variable t by the factor a causes an inverse scaling of the frequency variable ω by 1/a, as well as an amplitude scaling of X(ω/a) by 1/|a|.
  Thus, the scaling property implies that time compression of a signal (a>1) results in its spectral expansion and that time expansion of the signal (a<1) results in its spectral compression.

## Slide 24: Properties of Fourier transform
  Time Reversal:
  If time reversal of signal x(t) in time domain is x(-t), then in frequency domain the like reversal of X(ω) is X(- ω). That is
  x(-t)X(- ω)
  In time-scaling property, the case a = -1 leads to the time-reversal property.
  Convolution Property:
  The above equation is referred to as the time convolution theorem, and it states that convolution in the time domain becomes multiplication in the frequency domain.

## Slide 25: Properties of Fourier transform
  Differentiation in the Frequency Domain:
  Thus we see that, differentiation in the frequency domain property is the dual of differentiation in the time domain.
  Differentiation in the Time Domain:
  The above equation shows that the effect of differentiation in the time domain is the is the multiplication of X(ω) by jω in the frequency domain.

## Slide 26: Properties of Fourier transform
  Multiplication:
  The multiplication property is the dual property of convolution property.
  This property is often referred to as the frequency convolution theorem.
  Thus, multiplication in the time domain becomes convolution in the frequency domain.

## Slide 27: Properties of Fourier transform
  Additional Property:
  If x(t) is real, then it can be expressed as the sum of its even and odd components, i.e., x(t) = xe(t)+xo(t).
  Let, x(t) X(ω) + A(ω) +jB(ω).
  Then
  Equation (5.61a) is the necessary and sufficient condition for x(t) to be real.
  Equations (5.61b) and (5.61c) show that the Fourier transform of an even signal is a real function of ω and that the Fourier transform of an odd signal is a pure imaginary function of ω .

## Slide 28
  Parseval’s Property:
  Equation (5.64) is called Parseval's identity (or Parseval's theorem) for the Fourier transform.
  Note that the quantity on the left-hand side of Eq. (5.64) is the normalized energy content E of x(t). Parseval's identity says that this energy content E can be computed by integrating |X(ω)|2 over all frequencies ω. For this reason |X(ω)|2 is often referred to as the energy-density spectrum of x(t), and Eq. (5.64) is also known as the energy theorem. of ω .